## Slide 1: International Code of Safety for Maritime Autonomous Surface Ships: MASS Code
Gen Goto
May 14, 2026
CMI 2026 Rio de Janeiro

## Slide 2: MASS Code
Purpose
  Ensure safe, secure, and environmentally sound operation of MASS
  Support the adoption and integration of the new technology
  Provide for a consistent approach to the design, build, and operation of MASS
Supplements SOLAS and other IMO instruments
To achieve the levels of safety and security expected of a conventional ship
Goal-based standards at the functional level
  No numerical criteria
Technological neutrality

## Slide 3: Timeline
Non-mandatory MASS Code: expected to be adopted at MSC111 (May 13-22, 2026)
  MSC111/5/3 as the base text for consideration
Experience-building phase (EBP): 2026-2028
  List of items in MSC111/5/4
Work on MASS in other committees to resume
  LEG
  FAL
  MASS-JWG?
Mandatory MASS Code: amendment of SOLAS
  Start drafting in 2028
  Adoption: by July 1, 2030
  Entry into force: Jan 1, 2032

## Slide 4: Scope of application
Cargo ships to which SOLAS Chapter I applies, which have systems and functions that enable autonomous or remote operations
  Cargo ships on international voyages with 500 gross tonnage or over
  Passenger ships are excluded from the non-mandatory code
  Government-owned/operated vessels are excluded
Remote operation centers
Covers both autonomous operation and remote operation
  Degrees of automation are not defined
Applied regardless of whether persons are on board or not

## Slide 5: Structure of the Code
Part I: Introduction
Ch 1: Purpose, Principles, and Objectives
Ch 2: Application
Ch 3: Code Structure
Ch 4: Definitions
Part II: Main Principles for MASS and MASS Functions [and Remote Operations]
Ch 5: Surveys and Certificates
Ch 6: Approval Process
Ch 7: Risk Assessment
Ch 8: Operational Context
Ch 9: System Design
Ch 10: Software Principles
Ch 11: Management of Safe Operations
Ch 12: Alert Management
Ch 13: Manning, Training, and Watchkeeping
Ch 14: Maintenance
Part III: Goals, Functional Requirements, and Expected Performances
Ch 15: Safety of Navigation
Ch 16: Connectivity
Ch 17: Remote Operations
Ch 18: Structure, Subdivision, Stability, and Watertight Integrity
Ch 19: Fire Protection, Fire Detection, and Fire Extinction
Ch 20: Special Measures to Enhance Maritime Security
Ch 21: Search and Rescue
Ch 22: Carriage of Cargoes
Ch 23: Anchoring, Towing, and Mooring
Ch 24: Machinery and Electrical Installations

## Slide 6: How MASS Code will be applied: Chap 5-7
Risk assessment by the Company operating MASS
  Taking into account identified goals and functional requirements
The Administration of the flag state to conduct survey and approve
  Flag states to decide how to apply the requirements of the Code
The Administration to issue MASS certificate and ROC certificate (for each MASS the ROC operates)
  MASS record
    Description of the concept of operation (ConOps)
    ROCs approved for working with the MASS
  ROC record
    The MASS ConOps
    Operational restrictions on the ROC
    Infrastructure on connectivity and its performance and quality

## Slide 7: Safety management system: ISM Code Model 5.7 and Chap 11
Company operating MASS to develop and implement safety management system (SMS) on MASS and at ROC
Subdivision of tasks and relationship between the Company and ROC and MASS to be clearly indicated
SMS should provide for safe MASS operations, safety and well-being of personnels, and safety of MASS under all expected emergency conditions
Alternative SMS for ROCs to supplement MASS SMS

## Slide 8: Operational context: Chapter 8
Concept of operation (ConOps): how each MASS is intended to function
  Includes description on modes of operation (MoO)
Operational design domain (ODD): conditions under which a given function is designed to operate safely
  Systems should be able to detect whether their current state of operation meets ODD
  Deviation from ODD but within OE is considered as a degraded state
Operational envelope (OE): operational capabilities and limitations
  When deviating from OE, MASS enters a fallback state
  When a deviation goes beyond fallback states, contingency plans should be activated

## Slide 9: Human oversight and control: 8.7
All onboard and remote crew responsible for managing MASS operations should be able to exercise human oversight and control for operation of the MASS, including the ability to:
  understand and interpret system outputs;
  supervise the system, and verify system-initiated decisions, as appropriate; and
  intervene and/or override the system, if required.
Any onboard and remote crew responsible for managing MASS operations should always be able and prepared to take over the responsibilities of autonomous functions without risk to the outcome of the task.
There should be a human master responsible for a MASS, regardless of MoO, and the master should have the means to intervene when necessary.
The master and any onboard or remote crew should be provided ample time and sufficient information to be able to establish situational awareness, assume responsibility, and exercise direct or supervisory control of all functions according to the ConOps.

## Slide 10: Alert management: Chap 12
Alerts relevant for conventional ships: e.g. detection of dangerous objects
Alerts specific to MASS include, among others,
  Entering a fallback state or recognizing the need to enter a fallback state;
  Inability to enter a fallback state when deviating from its operational envelope;
  Equipment failure affecting operations of MASS functions or significantly increasing the risk of MASS operation e.g. loss of redundancy;
  System critical to MASS operation exceeds or is about to exceed its ODD;
  ROC-specific alerts (e.g. power failures, task station failures, communication system failures at ROC-level, software failures at ROC-level)
  Observation of abnormal situations and conditions concerning more than one MASS
When an emergency alarm is activated, a sufficient number of dedicated human operators including the master should be operating the MASS until the emergency is over.

## Slide 11: Manning, Training, and Watchkeeping Chap 13
Minimum safe manning to be specified by each MASS’s ConOps (5.9)
  Should be sufficient to ensure effective and efficient operation of MASS
  Unmanned MASS not excluded
Watchkeeping
  Could be performed by remote crew ROC without being physically present on board
  May be shared between onboard and remote crew, provided that clear lines of authority and responsibility are established between all watchkeeping personnel
Training of remote crew
  Remote crew should be qualified and competent to a level not less than required by STCW
  The Administration could consider STCW as applicable to ROC and remote crew

## Slide 12: Master of the MASS Chap 13
Regardless of the mode of operation, the master is responsible for the safe operation of the MASS at all times;
The master responsible for a MASS may be located physically onboard or at a ROC;
  If there is crew or persons on board, the master should be physically present on board to ensure the safety of personnel and operations;
Multiple masters may be operationally responsible for a MASS on a single voyage;
  Only one master should be responsible for a MASS at any given time
  Where command is transferred to or within a ROC, or between ROCs, sufficient time, resources and procedures should be provided to ensure that the master is fully familiar with the MASS and any ROC before assuming responsibility for the MASS.

## Slide 13: Safety of navigation: Chap 15
Voyage planning
  Use/modification of voyage plan requires an approval by the master
Situational awareness
  Continuous monitoring by the system
Collision and grounding risk avoidance
  Must comply with COLREG
Route execution and monitoring
  Must notify the master if at any time the prevailing circumstances and conditions necessitate a deviation from the voyage plan
Capability to override the system at all times from location(s) where control of navigation can be exercised

## Slide 14: What Comes Next?
Experience Building Phase: 2026-2028
Mandatory MASS Code
  Drafting from 2028
  Adoption planned in 2030
In the Legal Committee
  Examine the non-mandatory MASS Code to see if any concern for LEG arises
  Amendment/interpretation/guideline on implementation of LEG conventions?
  Civil liability regarding accidents by MASS?
    CMI’s proposal at LEG111 (April 2024)